## Slide 1
Network Automation
Network Automation
Network Automation

## Slide 2: Hughes
The connected future is here. It’s in upstate New Hampshire, where a freelance writer works online at home far from the city. It’s in Colombia, where a shop-owner sells affordable Wi-Fi and Internet access to rural villagers. It’s in the Southwest U.S., where a fast-casual restaurant chain can analyse data to improve the online experience for their customers. It’s in a military base in the Middle East, where service members connect with family and friends half a world away. It’s in the Congo, where a mobile network operator extends 3G cell service to customers in hard-to-reach places. It’s in India, where healthcare providers in towns and villages take online classes taught by experts from major urban clinics. It’s in the air, where travellers work or watch the latest movies and news, no matter where they are flying.
Making these connections is what Hughes is all about. We are industry leaders in both networking technologies and services, innovating constantly to deliver the global solutions that power a connected future for people, enterprises and things everywhere.
https://vimeo.com/258845721

## Slide 3: Key Pointers
Network and it’s importance
Internet Overview
How Browser search works?
Network terminologies
Network Automation and it’s scope
Python Overview and it’s need for Network automation
Library and functions of Python
Lab Check – Ping of remotes connected via Router

## Slide 4: Let’s Break it Down
Network
Automation
Python

## Slide 5: What is Networking?
Α network is simply defined as something that connects things together for a specific purpose. The term network is used in a variety of contexts, including telephone, television, computer, or even people networks.
A computer network connects two or more devices together to share a nearly limitless range of information and services, including:
• Documents
• Email and messaging
• Websites
• Databases
• Music
• Printers and faxes
• Telephony and videoconferencing

## Slide 6: Basic Network Terminologies
IP Address: An IP address, or simply an "IP," is a unique address that identifies a device on the Internet or a local network. It allows a system to be recognized by other systems connected via the Internet protocol.
Ping : Ping is a computer network administration software utility used to test the reachability of a host on an Internet Protocol network.
DNS : The Domain Name System is a hierarchical and decentralized naming system for computers, services, or other resources connected to the Internet or a private network. It associates various information with domain names assigned to each of the participating entities.
ARP: The Address Resolution Protocol is a communication protocol used for discovering the link layer address, such as a MAC address, associated with a given internet layer address, typically an IPv4 address.
Router: A router is a networking device that forwards data packets between computer networks. Routers perform the traffic directing functions on the Internet. Data sent through the internet, such as a web page or email, is in the form of data packets.
Mac Address : A media access control address is a unique identifier assigned to a network interface controller for use as a network address in communications within a network segment. This use is common in most IEEE 802 networking technologies, including Ethernet, Wi-Fi, and Bluetooth.
Default Gateway: A default gateway is the node in a computer network using the internet protocol suite that serves as the forwarding host to other networks when no other route specification matches the destination IP address of a packet.

## Slide 7: Example
1. ICMP creates an echo request payload
2. It then creates a packet with protocol field(01).The packet also contains source IP Address and destination IP Address
3. It checks whether the Destination IP address is on the local network,if not the packet needs to be sent to the default gateway.
4. The default gateway of PC1 is 172.16.10.1. For this the hardware address of router interface E0 must be known.
5. The PC1 will broadcast the ARP request to resolve the gateway IP into the hardware address.

## Slide 8: Example Contd…
6. Now the frame is generated encapsulating the packet. The frame will have PC1 hardware address and E0 hardware address as destination address.
7. The frame is then sent through the physical medium one bit at a time.
8. The gateway receives the bits, builds the frame,and checks the destination hardware address.
9. The packet is pulled from the frame. IP receives the packet and checks the destination IP, which doesn’t match with the gateway IP.So it will look into its routing table.
10. If there is an entry for the destination network, the packet is switched to the exit interface(E1)

## Slide 9: Example Contd…
11. Similarly the E1 needs to know the hardware address of the PC2.It will send a broadcast ARP to resolve the IP Address into hardware address.
12. Again the frame is created encapsulating the packet which contains the source hardware address as the hardware address of E1 and destination hardware address as of PC2.
13. Frame is sent to physical medium one bit at a time
14. PC2 receives the bit builds the frame, checks the destination hardware address, pulls the packet, and checks the destination address to be its own address.
15. The payload is handed to ICMP which understands that this is an echo request. It will discard the packet and generate the new payload as echo reply.
Same will continue for echo reply from PC2 to PC1.

## Slide 11: World with & without Network
Α network is simply defined as something that connects things together for a specific purpose. The term network is used in a variety of contexts, including telephone, television, computer, or even people networks.
A computer network connects two or more devices together to share a nearly limitless range of information and services, including:
• Documents
• Email and messaging
• Websites
• Databases
• Music
• Printers and faxes
• Telephony and videoconferencing